## Slide 1
6G 원천기술 후보
ETRI 6G 운영위원회(5차, 22년 3차)
2022. 7. 14.
네트워크연구본부
Notes: 발표를 시작하겠습니다.

## Slide 2: 6G 원천기술 목록 개요
원천기술명 | 제안자 | 특허 출원 여부
종단간 초정밀 네트워크 기술 개발 |  | 
Tbps급 광통신 인프라 기술 개발 |  | 
지능형 6G 모바일 코어 네트워크 기술 개발 |  | 
Cloud-Native 6G 모바일 코어 네트워크 기술 | 타이광퉁 | 8월 예정

## Slide 3: Cloud-Native 6G 모바일 코어 네트워크 기술(1/4)
  Our solution :
    Clear separation between data plane and control plane in signaling network
      Data plane: service – service interactions
      Control plane: configuring routes among services
    Service discovery/routing is implemented in a blackbox (integration fabric/service mesh) with simple APIs toward the network functions.
      Simplify signaling procedures within network functions
      Enable different kinds of service discovery
  Cloud-native 5G issues :
    Current architecture includes both mobile application network functions and service discovery/routing functions in the signaling network
    Complex signaling procedures within network functions due to the mixing of service discovery/service selection
    Centralized service discovery (bottleneck at NRF), high latency
    Prevent innovative approaches for service discovery

## Slide 4: Cloud-Native 6G 모바일 코어 네트워크 기술(2/4)
  Current service mesh solution
    Sidecar proxy is an independent application
    Incur latency due to more processing hops
    In current service mesh: service routing by names:
      find an instance of a service named http://example.com/web/backend
    In 5G:
      find and AMF that can serve slices A,B and C (difficult to realize with current service mesh)

## Slide 5: Cloud-Native 6G 모바일 코어 네트워크 기술(3/4)
  Invention description :
    The invention creates a service mesh of mobile core network functions. The mesh allows a network function can request a service from another network function by its name and description without knowing its location. The two network functions can be either in the same domain or in a different domain.
    The service mesh consists of a service controller and service agents. A service agent lives within a network function. Through the controller, agents learn each other locations which help them to direct service requests/responses to appropriate destinations.
Cluster
node
node
AMF
Service agent
Service Agent
SMF
node
pod
pod
Control plane
Data plane
Domain 1
Gateway
Service Agent
node
pod
Service Controller
Cluster
node
node
UDM
Service agent
Service Agent
UDR
node
pod
pod
Domain 2
Gateway
Service Agent
node
pod
Service Controller

## Slide 6: Cloud-Native 6G 모바일 코어 네트워크 기술(4/4)
Forwarder
Selection
Local Registry
Secure connection
Telemetry
Service Broker
Security Manager
Telemetry Manager
Policy Manager
6G Network Function Business Logic
(AMF, SMF, UDM, etc.
Or Service Gateway)
Service Agents
Control Plane
Data Plane
Other Network Functions
Configuration
  독창성 :
    A clear separation of control plane and data plane in mobile core signaling network
    Distributed service registry
    Essential complementary features (security, policy enforcement, telemetry) for the mobile core network can be implemented at the service agents
  (핵심성) Enables reliability, scalability, secured deployment of multi-domain network slicing
  (혁신성)
    Moving operational related features to service agent can simplify network function business logic which fosters the quick development of new applications.
    Service mesh and network functions can be developed independently
Service Controller

## Slide 7
)
AMF1
PCF1
SMF1
SMF2
PCFn
AMFn
UDM1
UDMn
New NF
New NF
-unified APIs interface
- alternative service discovery methods
- no centralized NRF → no bottleneck
- no NRF-bound → free to add new NFs
Integration fabric
(service registration, discovery, selection, fault detection

## Slide 8
register
nf-query
request
NF profiles
NRF
NF1
NF2
request
NF
X
response
Select NF
NF signaling logic
start agent
agent object
request + nf-query
Agent
response
request
Agent2
Announce
Update registry
Select NF
request
X
Agent1
API call/return
Network delivery message
register
nf-query
response
NF profiles
NF
NRF
SCP
NF1
NF2
X
request + nf-query
response
Select NF
Complex signaling procedures
Vendor-lockin (load balancing, telemetry, security, fault recovery)
1 hop service delivery
NRF dependent
Bottleneck at NRF
Simplified signaling
Unified load balancing, telemetry, security, fault recovery
2 hops service delivery
NRF dependent
Bottle neck at NRF
Simplified procedures
Unified Load balancing, telemetry, security, fault recovery
1 hop service delivery
No NRF, distributed registry (agents are registries)
request
request
response
5G/6G scope
5G/6G scope
5G/6G scope
Integration Fabric
Without SCP (TS 23.501 - model B)
With SCP (TS 23.501 - model D)
With an integration fabric
ack
ack
Network function boundary