## Slide 1: Method and apparatus for service mesh in cloud-native mobile core network
Quang Tung Thai, Namseok Ko

## Slide 2: 5G core network deployment challenges
The SBA decomposes the core network into small software components:
  Supports horizontal scaling, flexible deployments for network slicing
But, introduces deployment challenges:
  We may have 100x, 1000x instances of AMF, SMF in multiple clouds
AMF
SMF
PCF
UDM
UDR
AUSF
Conceptual network composition
AMF
AMF
AMF
SMF
SMF
AUSF
AMF
AMF
SMF
UDR
UDM
PCF
PCF
SMF
SMF
PCF
AMF
NRF
NRF
NRF
Service registration and discovery
Having various service discovery implementations at NFs creates a huge challenge for network deployments
Service registration and discovery
Service registration and discovery

## Slide 3: The root of this mess
Current architecture tries to solve two problems at the same time:
  Mobile applications (access, mobility, session management, charging etc .)
  Application deployment (service registration and discovery, slicing, security, scaling etc)
Consequences:
  Create confusions in deployment with four models (REL 16) (model A is not shown)
  Cumbersome signaling procedures:
    mixing service discovery logic with application signaling procedures
    leaving many gaps for custom of implementations -> vendor lock-in problems

## Slide 4: Complex signaling procedures
register
nf-query
request
NF profiles
NRF
NF1
NF2
request
NF
X
response
Select NF
register
nf-query
response
NF profiles
NF
NRF
SCP
NF1
NF2
X
request + nf-query
response
Select NF
Complex signaling procedures
Vendor-lockin (load balancing, telemetry, security, fault recovery)
Simplified signaling at the cost of extra delivery hop (at SCP)
Unified load balancing, telemetry, security, fault recovery
request
request
Without SCP (TS 23.501 - model B)
With SCP (TS 23.501 - model D)
ack
ack
Introduction of SCP (REL 16) confirms the existence of the deployment challenges
NRF bottleneck
NRF protocol-lock-in

## Slide 5: SCP Deployment Options
SCP based on service mesh
SCP based on independent deployment

## Slide 6: Service mesh SCP-based deployment

## Slide 7: What are the issues on the SCP
SCP is an optional (logical) component - no standardization
Incurs latency due to additional processing hops
  Relying on NRF for service discovery, not using the same feature supported natively by the service mesh. Why?
    In cloud-native service mesh: find an instance of a service named http://example.com/web/backend
    In 5G: find and SMF in slice A, B that serves data network ‘named etri’
  NRF is a bottleneck.
  NFs are bound to NRF. (NRF is in the application scope)

## Slide 8: Our solution
Creates an abstraction layer for handling service deployment logic
  The integration fabric is a black-box that implements service registration/discovery, connection security, fault –tolerance, traffic controlling etc.
  Unified APIs to NFs for simplifying signaling procedures
  Replace centralized NRF with a generic distributed registry.
    Scalable
    Extendable to deploy new services
)
AMF1
PCF1
SMF1
SMF2
PCFn
AMFn
UDM1
UDMn
New NF
New NF
Integration fabric
(service registration, discovery, selection, fault detection
Send a request to SMF in slice A, connecting to DN “etri-net”
Let me find all running instances that meet requirements
Let me do load balancing
Let me select the one is not dead
Here is a response
Send another request
Ok, just forward
Here is a response
NF’s signaling logic
Fabric – a black-box

## Slide 9: The integration fabric (a service mesh)
NFs are containerized and deployed in cloud platforms dynamically. The address of their running instances are ephemeral.
The service mesh allows NFs (same domain or cross-domain) can find each other seamlessly to request services.
The service mesh consists of a service controller and service agents. A service agent lives within an NF. Through the controller, agents learn each other locations which help them to direct service requests/responses to appropriate destinations.
AMF logic
Service agent
http
L1…L4
SMF logic
Service agent
http
L1…L4

## Slide 10: NF identification for discovery
NfType: amf,smf,udm, new-nf-type
PLMN: x,y,z
DNN: internet, etri, kisti
Slice: A, B, C, D
Region: Daejeon, Seoul, Busan
SubcriberGroup: g1,g2,g3
VerticalId: v1, v2, v3
(extendable dictionary)
AMF
PLMN: x
Slice: A, B
Region: Daejeon
VerticalId: v1
AMF
PLMN: x
Slice: A
Region: Seoul
VerticalId: v1
SMF
PLMN: x
Slice: A
Region: *
VerticalId: *
NF operating context
NF operating context
NF operating context
Context dictionary book
Network operators
defines
configures
Service consumer
conforms to
PLMN: x
Slice: A
Region: Daejeon
VerticalId: v1
Find AMF
NF query
Identifies an NF with an
Current architecture: NRF defines data models for each type of NFs; they are tightly coupled. NRF is within the application realm.
The fabric is application neutral. Network operators can defines contexts to deploy new applications. The registry system is outside of the application realm

## Slide 11: Distributed registry
  Controller is a registry broker that notifies agents of new updates.
    New agent announced its operating context, its location, and its contexts of interests (NF queries) to the broker
    The broker notifies only agents which are relevant to the announced updates
    Agents fetch full NF profiles from each other directly
  Agents keep a local partial registry database
    Registry DB is updated pro-actively
    Discovery can be done instantly (NF logic and agent operate in the same process)
    No bottleneck (as the case of using a centralized NRF)

## Slide 12: The fabric composition

## Slide 13: Service requesting
NF signaling logic
start agent
request 1 + nf-query
Agent
response 1
request 1
Agent2
Announce
Update registry
Select NF
request 1
X
Agent1
response 1
5G/6G scope
Network function boundary
start NF
request 2
request 2
response 2
response 2
Integration Fabric
Service discovery, security, signaling traffic steering, telemetry are handled by the integration fabric; transparently from the NFs’ perspective.
Simplified signaling logic
(focusing on application business logic)
forwarder
selector
registry manager
connection manager
telemetry
NF signaling logic layer
remote agent
1: request + nf-query
2: nf-query
3: nf-query
4: nf profiles
6: selected agent-id
7: get a connection to agent-id
8: a connection to agent-id
9: request
10: update telemetry data
11: response
12: response
13: update telemetry data
Complexity is moved into the agent module

## Slide 14: Significances the invention
Summary
  Proposed the integration fabric - encapsulating service discovery and routing
  A generic NF identification scheme for ease of integration of new applications
  Scalable instant service discovery with a distributed service registry
6G core will be a service-oriented network.
  Network functions should be plug-and-play
  Having an integration fabric is indispensable
The fabric enables additional features : security, fault-tolerance, telemetry for the network operators.
Observability is crucial to support native-AI 6G